## Slide 1
LIVE PARKING MAP
P
P
P
EMBEDDED SYSTEMS
Smart Parking
System
A wireless parking solution featuring an ESP-01 Wi-Fi module that detects free slots in real time, automates entry, and reports availability through a connected web dashboard.
Supervised by Dr. Amr Fahmy
Caroll Froid
Farida Elsayed
Norhan Mohamed
Zeina Mohamed

## Slide 2
01 · THE CHALLENGE
Problem Statement
Conventional parking is slow and blind and dangerously rigid when something goes wrong.
Wasted Time
Drivers circle for minutes hunting for an empty slot, especially at peak hours.
No Live Information
Neither drivers nor staff can see which spaces are free without checking each one.
Slow Manual Entry
Ticket-based or operator-run barriers create bottlenecks at the gate.
Emergency Risk
In a fire or emergency, the parking cannot be evacuated quickly manual gates stay shut and cars get trapped.

## Slide 3
02 · OUR ANSWER
Proposed Solution
An STM32-based system running FreeRTOS. IR sensors read every slot, RFID controls the gates, a flame sensor triggers automatic emergency opening, and an ESP-01 publishes live availability and exit receipts to a web dashboard.
Detect
IR slot sensors track every space as occupied or free.
Authenticate
RFID readers verify cards at the entry and exit gates.
Protect
A flame sensor fires the buzzer and opens the gates instantly in an emergency.
Inform
The LCD assigns a slot; the dashboard shows free spaces and prints an exit receipt.
SYSTEM FLOW
RFID / IR / Flame Sensors
▼
STM32 Blackpill + FreeRTOS
▼
ESP-01 Wi-Fi Module
▼
Web Dashboard
Ultrasonic /Servo Gate/LCD
▼

## Slide 4
03 · EQUAL CONTRIBUTION
Team & Task Organization
Every member owns an equal share of hardware, firmware and defense.
Caroll
Slots & Wireless
HARDWARE
IR sensor array; ESP-01 ↔ STM32; ESP-01 network connection checks
FIRMWARE
Poll slots (free/occupied); forward status to ESP-01→ save logs & auth roles to MongoDB
DEFENSE
Multi-zone pin scaling; wireless vs USB-TTL choice
Farida
Access & Structure
HARDWARE
Dual RC522 RFID on SPI; Ultrasonic
FIRMWARE
Read card UIDs; verify registered vs rejected cards;Ultrasonic GPIO
DEFENSE
SPI line-sharing (separate SS);
Norhan
UI & Integration
HARDWARE
I2C LCD (PB6/PB7); ESP-01 ↔ STM32; ESP-01 network connection checks
FIRMWARE
Web dashboard (HTML/CSS/JS); live slot colour updates;I2C
DEFENSE
Dashboard design; telemetry → database mapping
Zeina
Gates & Safety
HARDWARE
Servo gates; active buzzer & flame sensor
FIRMWARE
Servo PWM; flame interrupt → open→ Activate buzzer
DEFENSE
Gate actuation; zero-latency emergency handling
Shared by all four: FreeRTOS parallel-task architecture · GitHub repository & README

## Slide 5
04 • HOW WE BUILT IT
Work Steps & Outcomes
1
→
Assembling Entry, Exit & Display
Wired ultrasonic sensors, servo motors for both gates, the RFID reader/writer, and the I2C LCD building the core physical infrastructure.
✓
Functional gate & display hardware
2
→
Adding IR Sensors
Fitted IR sensors at each parking slot and beneath both gates for real-time occupancy detection and anti-crush safety.
✓
Car detection & anti-crush safety
3
Adding the ESP-01 (Wi-Fi)
Attached the ESP-01 module over UART, turning the standalone STM32 board into a connected device that streams live slot data wirelessly.
✓
Wireless, networked sensing
4
→
Building the Web UI
Coded the HTML/CSS/JS dashboard: a live slots map, exit receipt page, and admin view all updating in real time via the ESP-01.
✓
User & admin web pages
5
→
Maquette Assembly
Integrated all modules RFID gates, ultrasonics, servos, LCD, IR sensors, flame sensor and buzzer into a physical scale model, tested as one unified FreeRTOS system.
✓
Full working demo model
6
Standalone Power Supply
Connected a dedicated power source through a voltage regulator, making the system fully self-powered and independent of a laptop or USB connection.
✓
Laptop-free operation

## Slide 6
05 • WHAT IT DOES
Final Product Features
⊞
Real-Time Detection
IR sensors track each space and report free or occupied within seconds.
▣
LCD Slot Assignment
On entry, the driver is assigned a specific slot shown on the I2C LCD.
⊙
Automatic Gate Control
Ultrasonic sensors and servos open the barrier for an approaching car.
⊛
Anti-Crush Safety
The gate will not close while an IR sensor detects a car still beneath it and adds a penalty.
$
Penalty Charging
Fees are applied to vehicles that linger under the gate too long.
🔥
Fire Alarm & Buzzer
A flame sensor sounds the active buzzer and auto-opens the gates.
⊕
Live Slots Dashboard
A web page maps every free space and updates as the slot fills.
≡
Exit Receipt
After the car exits, the UI shows the driver a receipt for the visit.
⊡
Admin Panel
A dedicated admin view shows live occupancy, gate status, and system logs in real time.
★
Admin Card Access
The admin holds an RFID card that grants override control to open or close any gate instantly.
◈
VIP Card Access
VIP card holders are always directed to a reserved slot, even when the lot is full, with no fees charged.

## Slide 7
06 · UNDER THE HOOD
Technical Specifications
Component | Details
Main Controller | STM32 Blackpill running FreeRTOS
Wireless | ESP-01 Wi-Fi module over UART
Slot Sensors | IR sensors one per monitored space
Access Control | Dual RC522 RFID readers on a shared SPI bus
Gate System | Ultrasonic sensors + entry/exit servo motors
Safety | Flame sensor + active buzzer (auto gate open)
Display | I2C LCD (PB6/PB7) for slot assignment
Web Layer | HTML/CSS/JS dashboard served via ESP-01
Indicators | IR sensors & buzzers
Saving Logs | MongoDB
STM32
Blackpill core
ESP-01
Wi-Fi bridge
3.3 / 5 V
Dual power rails
FreeRTOS
Parallel tasks

## Slide 8
07 · THE PAYOFF
Achievements & Results
Reliable Detection
Slot status is reported accurately and consistently across the model.
Secure Access
RFID authentication admits only registered cards at both gates.
Emergency-Safe
Flame detection auto-opens the gates and sounds the buzzer with zero latency.
Hands-Free Flow
Cars are detected, assigned a slot and admitted without an operator.
Working Maquette
A complete scale model integrating every subsystem under FreeRTOS.
Live Dashboard
Real-time availability and exit receipts reachable from any browser.

## Slide 9
09 · THE PAPER TRAIL
Documentation
Everything needed to understand, rebuild and operate the system is documented and bundled with the project.
Project Report
Problem, design, build steps and final results.
Wiring & Block Diagrams
Pin maps, SPI/I2C/UART wiring and architecture.
Code Documentation
Commented STM32 firmware and FreeRTOS task notes.
User & Admin Manual
Using the dashboard, gates, receipts and overrides.
Project Repository
github.com/Norhanoraby/parking-system
Thank You
Scan to open